## Slide 1: Manchester SAFT
Overview

## Slide 2: What is SAFT?
State-of-the-art EoS for calculation of Helmholtz free energy
  Based on Wertheim perturbation theory
  Many flavours – we use SAFT-g-Mie
Basic form:
Additional terms can be added
  Ion interactions

## Slide 5
For current project, also require ion-ion interactions
  This comes in two parts at present
ABorn
  A Born term for the ion-solvent interactions
Aion
  Term for ion-ion interactions

## Slide 6: Program structure
MAIN
OPTIMISER
TYPES
GLOBAL
QUOTE
ZIG
INPUT
GL
INPUT_OPT
SIMPLEX
ERROR
DIFF
ION
ASSOC
CHAIN
MONO
IDEAL
SETUP
PHASE_SIMPLEX
ACT_ION
PURE_PHASE
VOL
PRESS
THERM
MU
ZEFF

## Slide 7: Program structure
Written in modules following FORTRAN standards
Modular design means
  Straightforward to find specific sections of code
  Simple to edit individual parts
  Many sections essentially “black boxes”
  Can write new driver program to interface with other software

## Slide 8: Program structure
Most parts are self-explanatory from names, and comments should be included
Some specific ones:
  Main
    This is the main program which reads input, performs requested calculation and prints output
  Optimiser
    This is the main program for running a parameter optimisation
  Global_mod
    This contains a list of globally used variables
    This saves passing large numbers of variables between modules!

## Slide 9: Capabilities
Many properties can be calculated from SAFT
  It is often straightforward to add modules for other properties
Currently included in this version:
Derivatives of A w.r.t. V and N are fully analytical (Diff_mod)
  Pressures and chemical potentials are precise (as is volume!)
Other derivatives are numerical
Pressure | Volume | Pure VLE
Parameter optimisation | Activity coefficient | Binary VLE
Chemical potential | Thermodynamic properties | CP

## Slide 10: Parameters
SAFT-g-Mie has quite a few parameters:
  s
  e (ii / ij)
  lr (ii / ij)
  la
  Sf
  Nseg
  mass
  EHB (ii / ij)
  KHB (ii / ij)
  dv
  dt
  q
  sborn

## Slide 11: Making & running the program
Brief user manual is included
TEST directory also has sample inputs
To make the code, use the Makefile
# make
  This uses the gfortran (gnu / gcc) compiler
  This will create mansaft.exe and optimiser.exe
On SCF, you will need to load the newer gfortran module!

## Slide 12: Making & running the program
To run a normal calculation:
./mansaft.exe input.in
To run a parameter optimisation:
./optimiser.exe input.in params.in
Note that .in files can have any names

## Slide 13: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS

## Slide 15: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS
Nsegments
Name s(Å) e(K) lr la Sf Nseg mass q sBorn Nassoc_types
Nassoc i

## Slide 16: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS
N unlike
segment i segment j e ij (K)

## Slide 17: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS
N unlike
segment i segment j l ij (K)

## Slide 18: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS
N assoc
segment i assoc_type k segment j assoc_type l EHB(K) KHB(Å3)

## Slide 19: Input file
TITLE
  BLANK
SEGMENTS
  BLANK
UNLIKE e
  BLANK
UNLIKE lr
  BLANK
ASSOCIATION
  BLANK
COMPONENTS
  BLANK
CALCULATION DETAILS
N molecule types
name mole_fraction mass dt dv number_segment_types
Segment_type number_of_segments

## Slide 20: Optimisation input
N parameters to optimise
KEY index_values min max
  Key is in manual, test inputs and Input_opt

## Slide 21: After September…
I have often altered the code
  I believe it should all be working, but….
  Any issues / questions with the program, please contact me:
Simon.halstead@gmail.com
My email is in code / manual too!
I am very keen for this code to be of use